## Slide 1
Particulate constituents such as POC and suspended sediment (SS) often show clockwise hysteresis, whereas DOC showed different hysteresis for different seasons, suggesting they are coming from different sources.
We are currently investigating these sources and constraining the exact timing of armor layer motion in each event.
The armor layer protects the finer bed subsurface from erosion, but when dislodged during high flow events it can release fine sediment enriched in Phosphorus (P) and Organic Carbon (OC).
Hysteresis and seasonal variations in particulate and soluble reactive phosphorus (PP and SRP) and in particulate and dissolved organic carbon (POC and DOC) could be controlled by armor layer motion
1University of Idaho, Boise, ID
2Utah State University, Logan, UT
3Los Alamos National Laboratory, Los Alamos, NM
Environmental System Science Program
Elowyn Yager1, Nicole Hucke1*, Rachel Watts2, Andrew Tranmer1, Janice Brahney2, Joel Rowland3, George Perkins3 and Rose Harris3
Introduction
Results
1. Capturing Hysteresis:
Study Site: La Jara Creek,
Valles Caldera National Preserve, NM
Laboratory Procedures
SS – Laser diffraction
method (LISST portable XR)
POC – Eurovector elemental analyzer coupled to an Isoprime IRMS
DOC – OI Analytical Aurora 1030 TOC Analyzer
SRP & PP – SpectraMax M2e
Water samples (SS, SRP, PP, DOC & POC)
Turbidity and fDOM*
Flow depth and Discharge
Stage-triggered portable ISCO samplers
Collected using a YSI EXO2 Sonde
* Fluorescent dissolved organic matter – a reliable proxy for DOC
Pressure transducers in stilling wells
2. Fine Sediment Deposition
Sediment traps with open and closed bottoms were installed next to subsurface temperature probes during the spring of 2023
Downwelling Conditions
Upwelling Conditions
Other deposition effects:
settling velocity
stream turbulence effects
3. Computing Hyporheic Flux
Through diel substrate water temperature fluctuations, we can solve the vertical flux from the 1D advection-diffusion equation using ΔA and ΔΦ.
Temperature-monitoring probes were installed at the locations of each basket group to estimate local hyporheic flux.
Methods
Results
For questions, please contact huck4481@vandals.uidaho.edu or eyager@uidaho.edu
Discussion and Further Work
Water Column Fine Sediment Concentrations and
Summer high flow events displayed a wider range of concentrations and higher peak concentrations on average than the spring event concentrations.
Spring high flow events have a wider range of D50’s and a coarser grain size distribution on average compared to the summer samples.
Average: | Spring | Summer
Concentration (μL/L) | 53.76 | 95.00
Median Grain Size (μm) | 65.74 | 54.65
Spring and Summer Fine Sediment Deposition
Results
Seasonal Constituent Hysteresis
Spring POC concentrations were too low that no reliable hysteresis could be obtained
A total of 7 summer and 4 snowmelt high flow events were captured for hysteresis
Particulate constituents (SS, POC and TP) exhibited clockwise hysteresis in the summer. SS behaved similarly in the spring
Dissolved constituents (DOC and SRP) differed in their behavior. Hysteresis for SRP changed for different summer storms. Hysteresis for DOC was consistently counter-clockwise in the summer and consistently clockwise in the spring. This suggests that these constituents might come from different sources
Coarser deposited grain sizes in the spring traps might be due to the transport of larger particle sizes and higher deposited sediment volume could be due to constant exposure to high flows compared to the summer storms.
Settling velocities for water column suspended sediment samples are yet to be calculated. A more comprehensive analysis of the sediment trap deposition of each grain size class (sand, silt and clay) with hyporheic flux is in development.
Different summer hysteresis patterns for DOC and particulate constituents suggest they are coming from different sources.
The different degree of hysteresis for particulates could be explained by the timing of armor layer motion. This timing is currently being explored to better understand our results
Impacts of streambed dynamics on nutrient and fine sediment transport in mountain rivers
Fine sediment deposition
Low Flow
Fines are protected by armor
Armor begins to move
Large Flow
Fines are released in water
A
B
C
D
or
Q
and
[C]
Time
Q
and
[C]
Time
Time
Q
and
[C]
Time
Q
and
[C]
The armor layer protects the finer bed subsurface from erosion, but when dislodged during high flow events it can release fine sediment enriched in Phosphorus (P) and Organic Carbon (OC).